## Slide 1
Upload files:
Loading and Saving EMG Data (from .mat to .txt)
Get only the last minute of data
Scale Signal to Microvolts
Preprocess signal:
Input: Raw EMG signal
Segment-based feature extraction
Input: .mat file  extract EMG & timestamps
Output: .txt  (channel 1 + timestamp)
nk.emg_clean: (20–450 Hz bandpass)
np.abs: rectifies the signal.
nk.signal_smooth: smooth the rectified signal
nk.emg_amplitude: estimates the amplitude envelope
Save processed features to file
Divides the EMG signal into equal-length segments.
Extracts 10 features per segment, using the pysiology library
Time-Domain: MAV, RMS, WL, ZC, IEMG, WAMP, VAR, LogD
Frequency-Domain: MNF, MDF
Output: A DataFrame with different signal transformations
EMG processing pipeline